## Slide 1
Deep Spectrum Sensing Under Realistic RF Conditions: A Cross-Dataset Study
ECCoLe
Edge Computing, Communication and Learning Lab
Atik Mahabub, Mouna Djellouli, and Shervin Vakili
INRS-EMT, Montreal, Canada
{atik.mahabub, mouna.djellouli, shervin.vakili}@inrs.ca
Presented By: Atik Mahabub
PhD, Student, INRS-EMT, Montreal, Canada
Email: atik.mahabub@inrs.ca
Date: May 19, 2026

## Slide 2
1. Research Objectives
Defining the core challenges in spectrum allocation and outlining the path to robust, machine learning-driven solutions.

## Slide 3
The rapid expansion of 5G and the impending dawn of 6G connectivity have placed unprecedented strain on the limited radio-frequency (RF) spectrum.
Cognitive Radio (CR) addresses this scarcity by enabling secondary users (SUs) to opportunistically utilize idle frequency bands without causing interference to primary users (PUs).
However, successful CR operation hinges on highly reliable spectrum sensing, particularly when signals are buried in severe noise (low SNR) and realistic channel fading.
The Cognitive Radio Imperative
5G

## Slide 4
6G
Imminent Deployment
Exploding Bandwidth Demand
As we transition into 6G networks, standard static frequency allocation is no longer sustainable.
The demand for bandwidth vastly outweighs the available spectrum allocations.
Dynamic, opportunistic access via CR is mandatory, requiring near-instantaneous and flawless detection of "empty" spectrum slots in increasingly noisy environments.
The Urgency of the RF Scarcity Problem

## Slide 5
Unified Formulation
Reformulate multiple diverse RF datasets into a standardized binary spectrum sensing task for direct comparability.
Cross-Dataset Eval
Test structural generalization by evaluating models across four distinct, heterogeneous datasets simultaneously.
Architecture Compare
Evaluate the strengths of four distinct DL architectures (CNN, LSTM, GRU, PETCGDNN) against traditional limits.
Core Study Objectives

## Slide 6
2. Novelty & Usefulness
Moving beyond synthetic idealized models to ensure structural generalization in harsh, real-world RF environments.

## Slide 7
The Generalization Gap
Many existing DL-based sensing models are structurally heavy and optimized exclusively for a single dataset. This prevents accurate assessment of their cross-dataset generalization and severely limits their feasibility for deployment on resource-constrained edge devices.
The Trivial Learning Trap
Conventional evaluations often represent "idle" channels using pure Additive White Gaussian Noise (AWGN). Models exploit this by learning simple signal-energy cues rather than recognizing complex RF modulation signatures, masking true performance drops.
Addressing Existing Limitations

## Slide 8
The Complex RF Baseline
To guarantee a rigorous stress test, we synthesized a standardized Complex RF Background Simulator.
Instead of pure AWGN, the idle class (Signal Absent) is flooded with realistic impairments, forcing the deep learning models to extract robust, discriminative modulation features rather than relying on trivial energy variances.
Colored Noise filtering
Random Narrowband Interference (NBI)
High-amplitude Impulsive Spikes

## Slide 9
3. Methodology Pipeline
A structured, end-to-end framework from dataset formulation to performance evaluation.

## Slide 10
Six-Phase DL-Based Evaluation Architecture

## Slide 11
Raw I/Q Sequences
Complex baseband In-Phase and Quadrature (I/Q) samples are fed directly into recurrent and complex-valued models. This preserves vital phase dynamics, temporal dependencies, and subtle waveform geometries critical for surviving low SNR environments.
Time-Frequency 2D
Short-time windows of I/Q samples are transformed into 2D representations (e.g., spectrograms) for the Convolutional models. This allows CNNs to leverage spatial-spectral filtering to detect localized energy signatures across different sub-carriers.
Feature Representations

## Slide 12
CNN Models
Focuses on spatial-spectral filtering and extracting visual-like patterns from frequency distributions
LSTM / GRU
Designed to strictly map temporal dependencies & complex sequence transitions over time
PETCGDNN
A lightweight, phase-aware network emphasizing extreme low-SNR robustness without memory bloat
Evaluated DL Architectures

## Slide 13
Architecture Deep-Dive

## Slide 14
Phase 5: Performance Evaluation
Analyzing model robustness and structural generalization across heterogeneous RF datasets under realistic channel impairments.

## Slide 15
Baseline Synthetic Immunity
Evaluated on 128×2 I/Q samples with size 1,200,000 over a SNR Range (-20dB to 18dB) against our Complex RF Background Simulator.
Low-SNR Resilience: LSTM achieves ~90% accuracy and >80% Probability of Detection (Pd) below -10dB.
Precision Leaders: PETCGDNN and CNN maintain superior precision across the entire spectrum.
Feature Isolation: Effectively isolates short-burst modulation features from NBI and impulsive spikes.
AUC Stability: Area Under the Curve (AUC) remains exceptionally high (>0.97) even in negative SNR regimes.
Results: RML2016b Dataset

## Slide 16
Results: RML2018a Dataset
Impaired Channel Recovery
Testing realistic impairments (multipath fading, CFO, hardware distortions) over longer 1024×2 I/Q samples with size 2,555,904 over a SNR Range (-20dB to 30dB) observation windows.
Standard Model Breakdown: At a severe -20 dB SNR, baseline LSTM exhibits a near 50% accuracy drop with only a 2.5% Probability of Detection (Pd).
PETCGDNN Recovery: Rebounds remarkably against multipath fading, achieving 100% Pd and >98% accuracy as SNR approaches +6dB.
Spatial Feature Extraction: CNN and hybrid layers proved critical here, mapping localized time-frequency distortions much more efficiently than purely sequential networks.

## Slide 17
Dynamic Mobile Environments
Subjected to time-varying channel conditions modeling Doppler effects and extreme multipath propagation.
Dataset: 1024×2 I/Q samples with size 780,000 over a SNR Range (-20dB to 18dB) observation windows.
Overall, Dominance: All evaluated models achieve exceptionally high performance across the entire SNR range.
LSTM Efficiency: Attains 99.3% accuracy and a “Pd” of 98.9% even at severe -20 dB noise floors.
Phase-Aware Precision: PETCGDNN maintains near-perfect F1-scores (>0.998) at all tested levels.
Separability: Distinct pulse shaping and constellations make signals easily separable from colored noise.
Results: HisarMod2019 Dataset

## Slide 18
Real-World Ionospheric Data
The ultimate stress test utilizing real over-the-air High-Frequency (HF) radio signals characterized by non-stationary noise.
Peak Accuracy: All four architectures successfully reach >99% accuracy at 0 dB SNR.
Domain Invariance: Models learned to recognize true domain-invariant phase and frequency transition patterns.
Generalization Check: Successfully classified complex physical HF signals against our purely synthetic interference baselines.
Results: PanoRadioHF Dataset
Dataset: 2048×2 I/Q samples with size 172,800 over a SNR Range (-10dB to 25dB) observation windows.

## Slide 19
*Table 2: CPU-only inference execution (Intel Core i7-13700, 32 GB DDR5 memory).
Computational Complexity & Latency

## Slide 20
Temporal Dominance
Phase-aware and recurrent models explicitly outperform others in deep low-SNR regimes, proving that tracking temporal correlations is critical to surviving multipath fading and CFO.
CNN Efficiency
Convolutional models provide extremely competitive accuracy at moderate-to-high SNRs, boasting parallel inference latency that benefits rapid real-time spectrum scanning operations.
Proven Generalization
By forcing models against a synthetic complex RF baseline, we prevented trivial energy detection, proving structural generalization across four vastly different data domains.
Key Research Conclusions

## Slide 21
SDR Validation
Transitioning from simulated inference to real-time over-the-air hardware validation using physical Software Defined Radio endpoints.
Transformer Networks
Exploring self-attention Transformer architectures specifically tuned for ultra-long sequence modeling across wideband spectra.
Edge Compression
Aggressive model quantization and compression designed to deploy lightweight cognitive capabilities directly onto IoT devices.
Future Research Outlines

## Slide 22
Questions?
Thank you for your attention
Institut national de la recherche scientifique (INRS-ÉMT) | Montreal, Canada